## Slide 1: Introduction to structured VLSI Projects 4 and 5
Rakesh Gangarajaiah
rakesh.gangarajaiah@eit.lth.se

## Slide 2: Objectives
Understand how to use the IP generator
Designing an interface with a memory and system integration
Fixed point programming and algorithm development from Matlab to Hardware implementation
Optimizing design for hardware resource constraints

## Slide 3: Overview of the system
GRADE 4
GRADE 5

## Slide 4: VGA controller

## Slide 5: VGA controller
Understand the VGA controller design.
  Modify parts of it to control the VGA display
  Create a driver for one 7 segment number display and re-use it to create others
  Remember that the square root will need an additional 7 segment displays

## Slide 6: VGA controller

## Slide 7: Project 4 - Calculator with Memory Objectives:
Integrate a 8k bit, 8bit wide RAM module to your ALU
Create/Update the VGA controller to display inputs and outputs on VGA screen
Input operands and operator from keyboard, store in RAM, fetch data and display results on VGA screen
Input operands are unsigned in the range of 0 to 255, but the result will be signed

## Slide 8: Xilinx LogiCoreIP generator
Read about the IP generator
Instantiate the memory following instructions from the manual

## Slide 9: Testing the RAM

## Slide 10: Expected operation : Data fill
Enter data from keyboard
Press data latch button
Addr 0
10
Addr 1
+
Addr 2
98
Addr 3
54
Addr 4
*
Addr 5
3
Direction of data fill
Addr 6
30
Addr 7
-
Addr 8
6

## Slide 11: Expected operation : Data retrieve and display
At every press of the <Enter> key
  Pop data
  Display result
Addr 0
10
Addr 1
+
Addr 2
98
Addr 3
54
Addr 4
*
Addr 5
3
Addr 6
30
Addr 7
-
Addr 8
6
006 – 030 = -024
003 * 054 = +162
VGA SCREEN
Direction of data POP

## Slide 12: Expected operation: Enter more operands
Should be able to accept new inputs
In the middle of data display
Enter operands from keyboard
  Press latch data
Addr 0
10
Addr 1
+
Addr 2
98
Addr 3
7
Addr 4
*
Addr 5
7
The next display on pressing the <Enter> key should be 007*007 = +049
VGA SCREEN
007 * 007 = +049
003 * 054 = +162

## Slide 13: Expected operation :

## Slide 14: Project 5: ALU with square root

## Slide 15: Objectives
Develop an algorithm for square root
  Implement in Matlab and verify with RTL output
Display result accurate to atleast 3 decimal digits
  Sqrt(111) = 10.535
  Sqrt(121) = 11.000
Do not use a look up table!!
The final implementation should be within a specified hardware resource utilization constraint. (More details in the manual)

## Slide 16: Square root unit
Different algorithms available to compute the square root
  Use Google, Wikipedia to find algorithms
Iterative algorithm
  Needs a simple state machine
  Make sure the decimal point is moved properly between states
Some of the algorithms need a division operation
  Use an IP to generate division outputs
Contact the TA before you finalize your algorithm

## Slide 17: Hardware utilization
Multipliers and dividers are usually needed for iterative algorithms
  Re-use as many as possible
Synthesize sqrt unit separately to enable the TA’s to check that you have met the resource constraints

## Slide 18: Divider
Use the LogiCore IP generator to generate a divider
  Discuss with TA about your choices of internal signal widths before starting
3 digits in decimal corresponds to 10 bits in binary
Test the divider unit separately before integrating

## Slide 19: Integration
Integrate the square root into the ALU unit
Final implementation should be able to accept square root as one of the operands (Use the key of your choice to indicate square root) and store it in the memory
Should display the results when enter keys are pressed just like in Project 4.