## Slide 1
EITF75 Systems and Signals
Lecture 1
Introduction
Fredrik Rusek

## Slide 2
EITF75 Systems and Signals
Schedule:
Lectures, F. Rusek, E:2377
12 lectures, 2/week
1 old exam solving
1 reserve
Exercises, G. Tian (E:2367), A. Sheikhi (E:2366)
14 exercises, 2/week
Labs, G. Tian, A. Sheikhi
2 Labs

## Slide 3
EITF75 Systems and Signals
Schedule:
Lectures, F. Rusek, E:2377
12 lectures, 2/week
1 old exam solving
1 reserve
Exercises, G. Tian (E:2367), A. Sheikhi (E:2366)
14 exercises, 2/week
Labs, G. Tian, A. Sheikhi
2 Labs
Self-study time
96 hours

## Slide 4
EITF75 Systems and Signals
Allowed tools:
Whatever you want to bring that does not have internet access
Two retake exams:
April, August
Exam gives maximum 5.0 points
Exam in
Systems and signals

## Slide 5
EITF75 Systems and Signals
Allowed tools:
Whatever you want to bring that does not have internet access
Two retake exams:
April, August
Exam gives maximum 5.0 points
There are two hand in assignements, these give 0.5p each
So, total points: 6.0
Hand in assignement
Nbr 1 (of 2)
Grades: 3.0-3.9: 3 4.0-4.9: 4 5.0-6.0: 5

## Slide 6
EITF75 Systems and Signals
Allowed tools:
Whatever you want to bring that does not have internet access
Two retake exams:
April, August
Exam gives maximum 5.0 points
There are two hand in assignements, these give 0.5p each
So, total points: 6.0
Hand in assignement
Nbr 1 (of 2)
Points from hand-in assignements valid for 1 year,
i.e., the October, April, and August exams

## Slide 7
EITF75 Systems and Signals
Allowed tools:
Whatever you want to bring that does not have internet access
Two retake exams:
April, August
Exam gives maximum 5.0 points
There are two hand in assignements, these give 0.5p each
So, total points: 6.0
Hand in assignement
Nbr 1 (of 2)
Deadline for handing in: end of September, mid-October (see web)

## Slide 8
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal

## Slide 9
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal
In reality, a signal is continuous.

## Slide 10
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal
The device has a task - it should output something
Output

## Slide 11
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal
Most general case is continuous output
Output

## Slide 12
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal
Obvious questions:
How should the device store/represent the signal ?
  - Almost impossible…
Output
Continuous memory…??

## Slide 13
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal
Obvious questions:
Suppose a Fourier transform of is needed.
How to compute for every ?
  -Almost impossible…
Output
Continuous memory…??
Further
Processing

## Slide 14
EITF75, Introduction
Consider an electronic device, observing a signal
Continuous time vs. Discrete time
Device
Signal
Summary
It is very hard for a computer to work with continuous signals
(Think for example of Matlab)
Output

## Slide 15
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Discrete signals:
Digital signals:
Continuous signals:

## Slide 16
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Discrete signals:
Digital signals:
Continuous signals: Simple…

## Slide 17
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Discrete signals: time is discrete, amplitude is continuous
1
2
3
Digital signals:
Continuous signals: Simple…

## Slide 18
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Continuous signals: Simple…
Discrete signals: time is discrete, amplitude is continuous
1
2
3
Digital signals: time is discrete, amplitude is discrete
1
2
3

## Slide 19
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Continuous signals: Simple…
Discrete signals: time is discrete, amplitude is continuous
1
2
3
Digital signals: time is discrete, amplitude is discrete
1
2
3
Essentially not treated in course.
However, the class of digital signals is a subset of the class of Discrete
signals, so everything we study
applies to digital signals as well

## Slide 20
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Continuous signals: Simple…
Discrete signals: time is discrete, amplitude is continuous
1
2
3
Where does a discrete signal appear in nature?

## Slide 21
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Continuous signals: Simple…
Discrete signals: time is discrete, amplitude is continuous
1
2
3
Where does a discrete signal appear in nature?
Nowehere (that I know). All natural signals are continuous/analog.
Discrete signals are man-made.
Examples:
Read temperature at constant interval
Read stock-price once/sec
Read an audio signal 44100 times/sec
Let a cell-phone read an incoming wave 10000000 times/sec
In all cases (except maybe stock price), the underlying signal is continuous, not discrete

## Slide 22
EITF75, Introduction
What is the difference between
Continuous signals
Discrete signals
Digital signals
Discrete time signals
Continuous signals: Simple…
Discrete signals: time is discrete, amplitude is continuous
1
2
3
Digital signals come about since it is hard for a computer to store all possible values. So it quantizes them.
We will briefly touch upon the losses involved in quantization
Digital signals: time is discrete, amplitude is discrete
1
2
3

## Slide 23
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
sampling
RAM
Processing

## Slide 24
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
sampling
RAM
Processing
Output can be either discrete or continuous

## Slide 25
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
sampling
RAM
Processing
Output can be either discrete or continuous
Reconstruction

## Slide 26
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
sampling
RAM
Processing
Output can be either discrete or continuous
Reconstruction
The target is to carry out the same task as an anolog device would
Device
Signal
Output
Continuous RAM
Processing

## Slide 27
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
sampling
RAM
Processing
Output can be either discrete or continuous
Reconstruction
The target is to carry out the same task as an anolog device would
Device
Signal
Output
Example: ”The output should be the mean of the input during the last 8 second plus the mean outputs during the last 5 seconds”

## Slide 28
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
RAM
Output can be either discrete or continuous
Thus, we need to understand how
Sampling should be done so that nothing is lost
How to process a discrete signal
How to convert a discrete signal into a continuous one so that it behaves well
Example: ”The output should be the mean of the input during the last 8 second plus the mean outputs during the last 5 seconds”
sampling
Processing
Reconstruction

## Slide 29
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
RAM
Output can be either discrete or continuous
sampling
Processing
Reconstruction
Chapters
1 Introduction
2 Discrete-Time Signals And Systems
3 The Z-Transform And Its Application To The Analysis Of LTI Systems
4 Frequency Analysis Of Signals And Systems
5 Frequency Domain Analysis Of Lti Systems
6 Sampling And Reconstruction Of Signals
7 The Discrete Fourier Transform: Its Properties And Applications
8 Efficient Computation Of The DFT: Fast Fourier Transform Algorithms
9 Implementation Of Discrete-Time Systems

## Slide 30
EITF75, Introduction
Discrete time signals
Device
Signal
Output
We study the following system
RAM
Output can be either discrete or continuous
sampling
Processing
Reconstruction
Chapters
1 Introduction
2 Discrete-Time Signals And Systems
3 The Z-Transform And Its Application To The Analysis Of LTI Systems
4 Frequency Analysis Of Signals And Systems
5 Frequency Domain Analysis Of Lti Systems
6 Sampling And Reconstruction Of Signals
7 The Discrete Fourier Transform: Its Properties And Applications
8 Efficient Computation Of The DFT: Fast Fourier Transform Algorithms
9 Implementation Of Discrete-Time Systems

## Slide 31
EITF75, Introduction
Some recap, notation and other basics
How we express a discrete signal
The bar below ”0” marks that this is at time n=0
1
2
3
0.5
1

## Slide 32
EITF75, Introduction
Some notation and basics
How we express a discrete signal
The bar below ”0” marks that this is at time n=0
1
2
3
0.5
1
system
Examples of systems
Easily understood as average of 5 last samples
Some recap, notation and other basics

## Slide 33
EITF75, Introduction
Some notation and basics
How we express a discrete signal
The bar below ”0” marks that this is at time n=0
1
2
3
0.5
1
system
Examples of systems
Easily understood as average of 5 last samples
But what does this system do? We’ll understand how to find out…
Some recap, notation and other basics

## Slide 34
EITF75, Introduction
Some notation and basics
How we express a discrete signal
The bar below ”0” marks that this is at time n=0
1
2
3
0.5
1
system
Examples of systems
Easily understood as average of 5 last samples
But what does this system do? We’ll understand how to find out…
Important class:
Feedback systems
0.9
Delay
What will happen ?
Some recap, notation and other basics

## Slide 35
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step

## Slide 36
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Signal is causal if it is zero for all negative indices

## Slide 37
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Signal is causal if it is zero for all negative indices
1
2
3
0.5
1
causal
1
2
3
not causal
-1
-2

## Slide 38
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Impulses and steps are key later, but for now we just mention that they can be used to mathematically represent a signal.
Examples:

## Slide 39
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Impulses and steps are key later, but for now we just mention that they can be used to mathematically represent a signal.
Examples:

## Slide 40
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
An expression of such form is important and is named convolution

## Slide 41
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Note that the below equality is obvious and only means
”a convolution with an impulse changes nothing”
However, this form will turn out to be useful later

## Slide 42
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Another example:
1
2
3
0.5
1
Can be written with step functions as…

## Slide 43
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Another example:
1
2
3
0.5
1

## Slide 44
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Another example:
1
2
3
0.5
1
1
2
3
0.5
1

## Slide 45
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Another example:
1
2
3
0.5
1
1
2
3
0.5
1
This is not correct,
since such signal is not causal

## Slide 46
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
1
2
3
0.5
1
Some recap, notation and other basics
Impulse
1
2
3
0.5
1
Step
Another example:
1
2
3
0.5
1
1
2
3
0.5
1
Like this

## Slide 47
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
Some recap, notation and other basics
Systems: delay
Expression
Circuit

## Slide 48
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
Some recap, notation and other basics
Systems: delay
Expression
Multiplication from now and on
Circuit
Circuit
Expression
What is the expression?

## Slide 49
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
Some recap, notation and other basics
Systems: delay
Expression
Circuit
Circuit
Expression
What is the expression?

## Slide 50
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
Some recap, notation and other basics
Systems: delay
Expression
Circuit
Circuit
Expression
What is the expression?

## Slide 51
EITF75, Introduction
Some notation and basics
Some important discrete signals and concepts
Some recap, notation and other basics
Systems: delay
Expression
Circuit
Expression
What is the expression?
Circuit

## Slide 52
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
In general, a signal generated
from via
can be mathematically described by
We will study this type of
systems in detail

## Slide 53
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal

## Slide 54
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Ohm’s law:
Power of signal:

## Slide 55
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Ohm’s law:
Power of signal:
So:
One measures the voltage using some equipment. Said equipment has
a resistance, , which does not change when the voltage changes.
Therefore, the power of two signals can be fairly compared using the square law.

## Slide 56
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Even symmetry
Odd symmetry

## Slide 57
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Even symmetry
Odd symmetry
Finite Memory
depends on
but not on
system

## Slide 58
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Even symmetry
Odd symmetry
Finite Memory
system
depends on
but not on
In words:
The output at time 106
does not depend on the input at time 0

## Slide 59
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Even symmetry
Odd symmetry
Finite Memory
depends on
but not on
Infinite Memory
depends on
In words:
The output at time 106
depends on the input at time 0

## Slide 60
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Energy of signal
Average power of signal
Even symmetry
Odd symmetry
Finite Memory
depends on
but not on
Infinite Memory
depends on
We will study why later….

## Slide 61
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Linear system
system

## Slide 62
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Linear system
system
system
system
system

## Slide 63
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Linear system
system
system
system
Holds for all linear systems
system

## Slide 64
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Linear system
Time invariant system
system

## Slide 65
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
Linear system
Time invariant system
system
system

## Slide 66
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
system
Linear system
Time invariant system
system
system

## Slide 67
EITF75, Introduction
Some notation and basics
Some recap, notation and other basics
system
Linear system
Time invariant system
BIBO-stability
BIBO = Bounded input,
bounded output

## Slide 68
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Amplitude
Frequency [Hz]
Phase [Rad]

## Slide 69
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Amplitude
Frequency [Hz]
Phase [Rad]
Period [s]

## Slide 70
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Amplitude
Frequency [Hz]
Phase [Rad]
Period [s]
Freq [Rad/s]

## Slide 71
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Amplitude
Frequency [Hz]
Phase [Rad]
Period [s]
Freq [Rad/s]
Delay [s]

## Slide 72
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Digital Freq [-]

## Slide 73
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Digital Freq [-]

## Slide 74
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Digital Freq [-]
Digital Freq [-]

## Slide 75
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Examples

## Slide 76
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Examples

## Slide 77
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Examples

## Slide 78
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Examples
No change

## Slide 79
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Examples
No change

## Slide 80
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
Explanation
No change

## Slide 81
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
No change
Explanation

## Slide 82
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
No change
Explanation

## Slide 83
EITF75, Introduction
Some notation and basics
Preliminaries of Sinusoids
No change
Important
Discrete sinusoid defined with a frequency
of at most ½ (or π rad) in magnitude
(Since higher frequencies than this don’t make any sense)

## Slide 84
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec

## Slide 85
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec
# Samples/sec [Hz]
Time between samples [s]
symbol
meaning
Ex. value

## Slide 86
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec
# Samples/sec [Hz]
Time between samples [s]
symbol
meaning
Ex. value

## Slide 87
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec
# Samples/sec [Hz]
Time between samples [s]
symbol
meaning
Ex. value

## Slide 88
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec
Sample with 1000 samples/sec

## Slide 89
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec
Sample with 1000 samples/sec

## Slide 90
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Sample with 1000 samples/sec
Sample with 1000 samples/sec
Sampling rate too low

## Slide 91
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Conclusion (verify this at home)
If
and we want a sampling Frequency such that we can
reconstruct from , then must satisfy

## Slide 92
EITF75, Introduction
Some notation and basics
Preliminaries of Sampling
RAM
sampling
Processing
Reconstruction
Conclusion (verify this at home)
If
and we want a sampling Frequency such that we can
reconstruct from , then must satisfy